10X（1/3〞）EFFIO-A系列 一体机机芯式样书

#### Model

FTZ10P70-T2E		FTZ10N70-T2E

#### Production

#### Specification

| Zoom Camera |
| --- |
| Model | FTZ10P70-T2E | FTZ10N70-T2E |
| Resolution | 700TVL | 700TVL |
| Communication mode | RS232 |
| Signal system | PAL/NTSC |
| CCD | 1/3" SONY CCD |
| Effective pixels | PAL:960(H)×582(V) / NTSC:967(H)×494(V) |
| Day & Night | Colour/ B&W /Auto/CDS |
| Mini.Illumination | 0.01Lux(infra LED on) |
| Sync System | Inter-sync |
| Video output | CVBS Output (1Vp-p-p75 Ω) |
| SNR | ≥48dB |
| Lens |
| FNO./Focal Length | F/2 f=5mm～50mm |
| IRCUT | IRCUT |
| AUTO IRIS | —— |
| FOV | H：51.8°（W）～5.86°（T） V：39.1°（W）～4.4°（T） |
| M.O.D | 0.5m（W）～1m（T） |
| Functions |
| OSD Display | Support |
| Lens Initialization | Auto |
| Exposure Mode | Auto/Manual |
| AWB | Auto/Indoor/Outdoor/Manual |
| Focus Mode | Auto/Manual |
| Picture Effects | Auto/Color/B&W/Negative |
| Backlight Compensator | Support |
| Contrast | Support |
| Saturation | Support |
| Mirror Image | Support |
| Digital Zoom | Support |
| Freeze | Support |
| Rollovers | Support |
| WDR | D-WDR |
| DNR | 2D/3D-DNR |
| General Specifications |
| Size | 38.6（W）* 41（H）* 64.6（L） mm |
| Working Temp./Hygro. | ﹣10℃～50℃，10％RH～60％RH |
| Storage Temp./Hygro. | ﹣20℃～60℃，10％RH～80％RH |
| Power Voltage | DC 12V±10% |
| Power consumption | 2.5W MAX |
| Net Weight | 100g |

#### Pin assignment

The Connect Pins Functions Table: the order of 1 to 9 pin location and the following table.

| Pin NO. | Name | Specification |
| --- | --- | --- |
| ( | RxD | CMOS 3.3V (low: max 0.8V, high: min 2.8V) Read Date |
| ( | TxD | CMOS 3.3V (low: max 0.8V, high: min 2.8V) Send Date |
| ( | GND (for RxD&TxD) |  |
| ( | DC IN | 12V±3V |
| ( | GND (for DC IN) |  |
| ( | VBS OUT | 1.0V±0.2V |
| ( | GND (for VBS OUT) |  |
| ( | NC |  |
| ( | GND |  |

#### 菜单说明：

第一页：

>	语言			中文

地址			01~07

波特率			1200/2400/4800/9600/14400/19200/38400/56000/57600/115200/

OSD显示		关/开

地址显示		关/开

数字放大		关/开

日夜切换		自动/彩色/黑白/CDS

彩-黑			00~31

黑-彩			00~31

镜像			关/左右/上下/左右+上下

第二页：

曝光			自动/手动/光圈优先/快门优先/

DSS			00

光圈		00

快门		00~07

增益		00~07

自动增益		00~31

亮度			00~31

对比度			00~31

锐度			00~31

SAT				00~31

第三页：

宽动态			关/低/中/高

2D降噪			00~04

3D降噪			00~04

白平衡			自动/ATW/PUSH/HOLD/CRS/FLUO/室内/室外/MANU/USER

红色增益	00~255

蓝色增益	00~255

透雾			00~03

视频			CRT/LCD

背光补偿		关/开

强光抑制		00~13

第四页：

ZOOM			02~50

DZOOM			02~100

FOCUS			自动/手动

ZOOM保存		开/关

FOCUS位置		>1.3M/2.1M/4.7M/10M

ZOOM显示位置	右下/右上/左下/左上+1/左上+2/右下-1/右下-2/右上-1/右上-2/左下+1/左下+2/左上/

复位

保存退出

英文菜单：

First Page：

LANG			EN

ADDR			00~07

BAUD			1200/2400/4800/9600/14400/19200/38400/56000/57600/115200/

OSD-DISP		OFF/ON

ADDR-DISP		OFF/ON

D-ZOOM			OFF/ON

D&N			AUTO/COL/BW/CDS

D&N-LV			00~31

N&D-LV			00~31

MIRROR			OFF/LR/UD/FLIP

Second Page:

AE				AUTO/MANUAL/IRIS/SHUTT

DSS			00

IRIS			00

SHUTTER	00~07

GAIN		00~07

AGC			00~31

BRIGHT			00~31

CONTRAST		00~31

SHARPNESS		00~31

SAT				00~31

Third Page:

ATR				OFF/LOW/MID/HIGH

2D-NR			00~04

3D-NR			00~04

WB				AUTO/ATW/PUSH/HOLD/CRS/FLUO/IN/OUT/MANU/USER

RGAIN		00~255

BGAIN		00~255

DE-FOG			00~03

MONITOR		CRT/LCD

BLC				OFF/ON

HLC			00~13

Fourth Page:

ZOOM			02~50

DZOOM			02~100

FOCUS			AF/MF

Z-SAVE			OFF/ON

F-RANGE		>1.3M/2.1M/4.7M/10M

ZDISP-POS		RD/RU/LD/LU+1/LU+2/RD-1/RD-2/RU-1/RU-2/LD+1/LD+2/LU/

RESET

SAVE-EXIT

菜单操作

进入菜单指令：81 01 04 DF 01 FF

退出菜单指令：81 01 04 DF 00 FF

向上移动菜单选项指令：81 01 04 07 02 FF

向下移动菜单选项指令：81 01 04 07 03 FF

更改菜单选项指令：81 01 04 08 02/03 FF

菜单说明：

在菜单中更改任何选项，必须要在最后一页菜单中选择保存退出，更改才会生效，如果直接退出菜单更改不生效，当在菜单中选择复位时，系统状态恢复到出厂默认值

## Command List

## （注明：命令中红色标记项为可选项，根据产品型号对应功能。）

#### Function Command List

| Command Set | Command | Command Packet | Comments |
| --- | --- | --- | --- |
| Network Change | Broadcast | 88 30 0x FF |  |
| IF_Clear | Broadcast | 88 01 00 01 FF |  |
| CAM_Power | On | 8x 01 04 00 02 FF | Power ON/OFF |
|  | Off | 8x 01 04 00 03 FF |  |
| CAM_Zoom | Stop | 8x 01 04 07 00 FF |  |
|  | Tele(Standard) | 8x 01 04 07 02 FF |  |
|  | Wide(standard) | 8x 01 04 07 03 FF |  |
|  | Tide(Variable) | 8x 01 04 07 2p FF | 速度与Standard相同，不可变 |
|  | Wide(Variable) | 8x 01 04 07 3p FF |  |
|  | Direct | 8x 01 04 47 0p 0q 0r 0s FF | pqrs: Zoom Position |
| CAM_DZoom | On | 8x 01 04 06 02 FF | Digital zoom ON/OFF |
|  | Off | 8x 01 04 06 03 FF |  |
|  | Combine Mode | 8x 01 04 36 00 FF | Optical /Digital Zoom Combined |
|  | Separate Mode | 8x 01 04 36 01 FF | Optical /Digital Zoom Separate |
|  | Stop | 8x 01 04 06 00 FF |  |
|  | Tele (Variable) | 8x 01 04 06 2p FF | p=0 (Low) to 7 (High) |
|  | Wide (Variable) | 8x 01 04 06 3p FF |  |
|  | x1/Max | 8x 01 04 06 10 FF | x1/Max Magnification Switchover |
|  | Direct | 8x 01 04 06 00 00 0p 0q FF | pq: D-Zoom Position |
| CAM_Focus | Stop | 8x 01 04 08 00 FF |  |
|  | Far(Standard) | 8x 01 04 08 02 FF |  |
|  | Near(Standard) | 8x 01 04 08 03 FF |  |
|  | Far(Variable) | 8x 01 04 08 2p FF | 速度与Standard相同，不可变 |
|  | Near(Variable) | 8x 01 04 08 3p FF |  |
|  | Direct | 8x 01 04 48 0p 0q 0r 0s FF | pqrs: Focus Position |
|  | Auto Focus | 8x 01 04 38 02 FF | AF ON/OFF |
|  | Manual Focus | 8x 01 04 38 03 FF |  |
|  | Auto/ Manual | 8x 01 04 38 10 FF |  |
|  | One Push Trigger | 8x 01 04 18 01 FF |  |
|  | Infinity | 8x 01 04 18 02 FF |  |
|  | Near Limit | 8x 01 04 28 0p 0q 0s FF | pqrs: Focus Near Limit Position |
| AF Sensitivity | Normal | 8x 01 04 58 02 FF | AF Sensitivity High/Low |
|  | Low | 8x 01 04 58 03 FF |  |
| CAM_AF Mode | Normal AF | 8x 01 04 57 00 FF | AF Movement Mode |
|  | Interval AF | 8x 01 04 57 01 FF |  |
|  | ZoomTriggerAF | 8x 01 04 57 02 FF |  |
|  | Active/Interval Time | 8x 01 04 27 0p 0q 0r 0s FF | pq:Movement Time, rs:Interval |
| CAM_Zoom Focus | Direct | 8x 01 04 47 0p 0q 0r 0s 0t 0u 0v 0w FF | pqrs: Zoom Position tuvw: Focus Position |
| CAM_Initialize | Lens | 8x 01 04 19 01 FF | Lens Initialization start |
| CAM_WB | Auto | 8x 01 04 35 00 FF | Normal Auto |
|  | Indoor | 8x 01 04 35 01 FF | Indoor mode |
|  | Outdoor | 8x 01 04 35 02 FF | Outdoor mode |
|  | ATW | 8x 01 04 35 04 FF | Auto |
|  | Manual | 8x 01 04 35 05 FF | Manual Control mode |
| CAM_R Gain | Reset | 8x 01 04 03 00 FF | Manual Control of R Gain |
|  | Up | 8x 01 04 03 02 FF |  |
|  | Down | 8x 01 04 03 03 FF |  |
|  | Direct | 8x 01 04 43 00 00 0p 0q FF | pq: R Gain |
| CAM_B Gain | Reset | 8x 01 04 04 00 FF | Manual Control of B Gain |
|  | Up | 8x 01 04 04 02 FF |  |
|  | Down | 8x 01 04 04 03 FF |  |
|  | Direct | 8x 01 04 44 00 00 0p 0q FF | pq: B Gain |
| CAM_AE | Full Auto | 8x 01 04 39 00 FF | Automatic Exposure mode |
|  | Manual | 8x 01 04 39 03 FF | Manual Control mode |
| CAM_Gain | Reset | 8x 01 04 0C 00 FF | Gain Setting |
|  | Up | 8x 01 04 0C 02 FF |  |
|  | Down | 8x 01 04 0C 03 FF |  |
|  | Direct | 8x 01 04 4C 00 00 0p 0q FF | pq: Gain Position |
| CAM_Backlight | On | 8x 01 04 33 02 FF | Back Light Compensation ON/OFF |
|  | Off | 8x 01 04 33 03 FF |  |
| CAM_LR_ Reverse | On | 8x 01 04 61 02 FF | Mirror Image ON/OFF |
|  | Off | 8x 01 04 61 03 FF |  |
| CAM_Freeze | On | 8x 01 04 62 02 FF | Still Image ON/OFF |
|  | Off | 8x 01 04 62 03 FF |  |
| CAM_Picture Effect | Off | 8x 01 04 63 00 FF | Picture Effect Setting |
|  | Neg.Art | 8x 01 04 63 02 FF |  |
|  | B&W | 8x 01 04 63 04 FF |  |
| CAM_PictureFlip | On | 8x 01 04 66 02 FF | Picture flip ON/OFF |
|  | Off | 8x 01 04 66 03 FF |  |
| CAM_ICR | On | 8x 01 04 01 02 FF | Infrared Mode ON/OFF |
|  | Off | 8x 01 04 01 03 FF |  |
| CAM_AutoICR | On | 8x 01 04 01 02 FF | Auto Infrared Mode ON/OFF |
|  | Off | 8x 01 04 01 03 FF |  |
| CAM_Memory | Reset | 8x 01 04 3F 00 0p FF | p: Memory Number (=0 to 5) |
|  | Set | 8x 01 04 3F 01 0p FF |  |
|  | Recall | 8x 01 04 3F 02 0p FF |  |
| CAM_CUSTOM | Reset | 8x 01 04 3F 00 7F FF | Starts in this mode at Power ON. |
|  | Set | 8x 01 04 3F 01 7F FF |  |
|  | Recall | 8x 01 04 3F 02 7F FF |  |
| CAM_MemSave | Write | 8x 01 04 23 0X 0p 0p 0q 0q FF | X: 00 to 07 (Address) Total 16 Byte ppqq: 0x0000 to 0xFFFF (Data) (Xpq参数未解析,保存机芯所有参数) |
| CAM_Display | On | 8x 01 04 15 02 FF | Display: ON/OFF |
|  | Off | 8x 01 04 15 03 FF |  |
|  | On/Off | 8x 01 04 15 10 FF |  |
| CAM_Title | Title Set1 | 8x 01 04 73 00 mm nn pp qq 00 00 00 00 00 00 FF | mm:Vposition, nn:Hposition, pp:Color, qq:Blink |
|  | Title Set2 | 8x 01 04 73 01 mm nn pp qq rr ss tt uu vv ww FF | mnpqrstuvw:Setting of Display Characters(1st to10st Character ) |
|  | Title Set3 | 8x 01 04 73 02 mm nn pp qq rr ss tt uu vv ww FF | mnpqrstuvw: Setting of Display Characters(11st to 20st Character) |
|  | Title Clear | 8x 01 04 74 00 FF | Title Setting Clear |
|  | On | 8x 01 04 74 02 FF | Title Display ON/OFF |
|  | Off | 8x 01 04 74 03 FF |  |
| CAM_Mute | On | 8x 01 04 75 02 FF | Mute ON/OFF |
|  | Off | 8x 01 04 75 03 FF |  |
|  | On/Off | 8x 01 04 75 10 FF |  |
| CAM_ID Write |  | 8x 01 04 22 0p 0q 0r 0s FF | pqrs: Camera ID (=0000 to FFFF) |

#### Inquiry Command List

| Inquiry Command | Command Packet | Inquiry Packet | Comments |
| --- | --- | --- | --- |
| CAM_PowerInq | 8x 09 04 00 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_ZoomPosInq | 8x 09 04 47 FF | y0 50 0p 0q 0r 0s FF | pqrs:ZoomPosition |
| CAM_DZoomModeInq | 8x 09 04 06 FF | y0 50 02 FF | D-Zoom On |
|  |  | y0 50 03 FF | D-Zoom Off |
| CAM_DZoomC/SModeInq | 8x 09 04 36 FF | y0 50 00 FF | Combine Mode |
|  |  | y0 50 01 FF | Separate Mode |
| CAM_DZoomPosInq | 8x 09 04 46 FF | y0 50 00 00 0p 0q FF | Pq: D-Zoom Position |
| CAM_FocusModeInq | 8x 09 04 38 FF | y0 50 02 FF | Auto Focus |
|  |  | y0 50 03 FF | Manual |
| CAM_FocusPosInq | 8x 09 04 48 FF | y0 50 0p 0q 0r 0s FF | pqrs:FocusPosition |
| CAM_FocusNear LimitInq | 8x 09 04 28 FF | y0 50 0p 0q 0r 0s FF | pqrs: Focus Near Limit Position |
| CAM_AFModeInq | 8x 09 04 57 FF | y0 50 00 FF | Normal AF |
|  |  | y0 50 01 FF | Interval AF |
|  |  | y0 50 02 FF | Zoom Trigger AF |
| CAM_AFTime SettingInq | 8x 09 04 27 FF | y0 50 0p 0q 0r 0s FF | pq: Movement Time, rs: Interval |
| CAM_WBModeInq | 8x 09 04 35 FF | y0 50 00 FF | Auto |
|  |  | y0 50 01 FF | In Door |
|  |  | y0 50 02 FF | Out Door |
|  |  | y0 50 05 FF | Manual |
| CAM_RGainInq | 8x 09 04 43 FF | y0 50 00 00 0p 0q FF | pq: R Gain |
| CAM_BGainInq | 8x 09 04 44 FF | y0 50 00 00 0p 0q FF | pq: B Gain |
| CAM_AEModeInq | 8x 09 04 39 FF | y0 50 00 FF | Full Auto |
|  |  | y0 50 03 FF | Manual |
|  |  | y0 50 0B FF | Iris Priority |
| CAM_GainPosInq | 8x 09 04 4C FF | y0 50 00 00 0p 0q FF | pq: Gain Priority |
| CAM_BacklightModeInq | 8x 09 04 33 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_LR_ReverseModeInq | 8x 09 04 61 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_FreezeModeInq | 8x 09 04 62 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_PictureEffectModeInq | 8x 09 04 63 FF | y0 50 00 FF | Off |
|  |  | y0 50 02 FF | Neg.Art |
|  |  | y0 50 04 FF | B&W |
| CAM_PictureFlipModeInq | 8x 09 04 66 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_ICRModeInq | 8x 09 04 01 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_AutoICRModeInq | 8x 09 04 51 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_MemoryInq | 8x 09 04 3F FF | y0 50 pp FF | pp: Last Recall Memory No. |
| CAM_MemSaveInq | 8x 09 04 23 0x FF | y0 50 0p 0p 0q 0q FF | X:00～07(Address) ppqq: 0x0000 to 0xFFFF (Data) |
| CAM_DisplayModeInq | 8x 09 04 15 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_MuteModeInq | 8x 09 04 75 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_TitleDisplay ModeInq | 8x 09 04 74 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_IDInq | 8x 09 04 22 FF | y0 50 0p 0q 0r 0s FF | pqrs: Camera ID |

Zoom Ratio and Zoom Position (for reference) Zoom Ratio x10 Lens Optical Zoom Position Data X1 0000 X2 0BBD X3 175D X4 21C0 X5 2C77 X6 3592 X7 3B86 X8 3E38 X9 3FA7 X10 4000

菲特机芯查询命令：

| 自检查询机器型号 | 查询命令 | 返回码 | 注释 |
| --- | --- | --- | --- |
| pp qq | 81 09 04 B2 FF | 90 50 B2 pp qq FF | 1011：FTZ10P70-T2E 1021：FTZ10N70-T2E |
| 深圳市菲特数码技术有限公司 |
| 地址：深圳市南山区西丽镇牛成村牛成路221号5楼 |
| 电话：0755-26414937 传真：0755-86181786 |
| Email：fitech@fitech.cn 网站：www.fitech.cn |

# Text boxes

(

((

((((((

Command List