10X/18x（1/3〞）SDI CAMERA SPECIFICATION

#### Model

FTG10H72-T4  FTG10H108-T4  FTG18H72-T4      FTG18H108-T4

#### Production Size

10X:

18X:

#### Specification

| Camera |
| --- |
| Model | FTG10H72 | FTG18H72 | FTG10H108 | FTG18H108 |
| Interface | RS485 |
| Communication | Pelco.D/P |
| Sensor | 1/3" SONY CMOS |
| Resolution | HD720P:1280(H)X720(V) | HD1080P:1920(H)X1080(V) |
| Day&Night | Color/B&W/Auto |
| Mini Illumination | 0.01Lux(infra LED on) |
| Sync System | Inter-sync |
| Video output | SDI Output |
| SNR | ≥48dB |
| Lens |
| Lens Focal Length | 10X:f=5mm～55mm 18X:f=5mm～90mm |
| IRCUT | IRCUT |
| AUTO IRIS | —— |
| FOV | 10X: 47°（W）～5.3°（T） V：35.6°（W）～3.96°（T） 18X: H：52.5°（W）～3°（T） V：40°（W）～2.3°（T） |
| M.O.D | 0.2m（W）～1m（T） |
| Function |
| OSD | Support |
| Lens Initialisation | Auto |
| Exposure Mode | Auto/Manual |
| AWB | Auto/Indoor/Outdoor/Manual |
| Focus Mode | Auto/Manual |
| Picture Effects | Auto/Color/B&W/Negative |
| Backlight Compensator | —— |
| Contrast | Adjust |
| Saturation | Adjust |
| Mirror Image | Support（LR+UD） |
| D-Zoom | —— |
| Freeze | —— |
| Rollovers | Support |
| WDR | D-WDR |
| DNR | 2D-DNR |
| Specification |
| Size | 10X:56（W）* 56（H）* 97（L） mm 18X: 60（W）* 63（H）* 115（L） mm |
| Working Temp./Hygro. | ﹣10℃～50℃，10％RH～60％RH |
| Storage Temp./Hygro. | ﹣20℃～60℃，10％RH～80％RH |
| Power Voltage | DC 12V±10% |
| Power consumption | 3W MAX. |

#### BOARD INTERFACE:

10X:

18X:

#### INTERFACE explain

| Interface | Name | Function |
| --- | --- | --- |
| Menu | M | Open/Switch Menu |
|  | W | ZOOM in/Move cursor upward in Menu |
|  | T | ZOOM out / Move cursor downward in Menu |
|  | F | Focus far/Modify setup in menu |
|  | N | Focus near/ Modify setup in menu |
| PWR LED | PWR | Light on means PWR ON, Light off means PWR OFF |
| Video output | VIDEO | SDI OUTPUT |
| 485 120R Resistor match | ON | Resistor Connect |
|  | OFF | Resistor does Not connect |
| 485 Signal | A | RJ85A |
|  | B | RJ85B |
| POWER | + | Connect 12V positive |
|  | - | Connect 12V negative |

INSTALL

        - Fixed the camera on the bracket；

        - Connect the VIDEO；

        - Connect DC12V power ；

        - Adjust the camera aim at the target.

Menu

FTG10H72/FTG10H108/ FTG18H72/FTG18H108 OSD menu

Page 1：

LANG                 EN

ADDR                 01

BAUD                 9600

OSD-DISP              ON/OFF

OEM-ZOOM            18

FOCUS                 AF/MF/TRIG

D&N                   AUTO/COL/BW

D&N-LV                0～31

N&D-LV                0～31

MIRROR 	             OFF/LR/UD/FLIP

OUTPUT                1080P@25 / 1080P@30 / 720P@25 /720P@30

Page 2：

IRIS                     AUTO

WB                     ATW/FULL/HOLD

WDR                    ON/OFF

AGC                     0~31

2D-NR                   0～5

BRIGHT	               0-31

CONTRAST               0-31

SATURATION             0-31

SHARPNESS              0-31

RESET

SAVE-EXIT

# Text boxes

Command List

T

F        N

PWR    120R

VIDEO

ON    OFF

LINE  485 POWER

M Z F C B A－+

W

M

T

F   M   N

PWR    120R

VIDEO

ON    OFF

LINE  485 POWER

M Z F C B A－+

W

Command List

Command List